## Slide 1: CEN511: EMBEDDED SYSTEMS DESIGN AND PROGRAMMING
COURSE LECTURERS
ODUSAMI MODUPE (Engr.)
OMORUYI OSEMWEGIE

## Slide 2: Topics
Instruction Set and Assembly Language Programming: Addressing modes,
The 8051 instruction set and typical examples,
Assembler operation, assembly language format, assembler directives, operation of assemblers and linkers,
Programming examples in Assembly and Embedded c.

## Slide 3: 8051 Instruction Set and Assembly Language Programming
Definition of Terms
Mnemonic: a given or singular instruction in a CPUs instruction set.
Opcode: the part of a mnemonic that specifies the operation to be carried out.
Operand: the part of an instruction that specifies the data or memory location to act on.

## Slide 4: Data Movement in 8051
The 8051 has 28 distinct mnemonics in its Assembly language for moving Data.
There are three main opcodes for data movement namely:
MOV dest., source
XCH dest., source
PUSH source or POP dest.
The other mnemonics are often a variation of the above listed three.

## Slide 5: Addressing modes
The 8051 has four addressing modes:
Immediate- When the source is a part of the instruction. Often times the source is an operand or value to be stored in a destination. The mnemonic for an immediate value is the (#) sign. However, assemblers may accept operand values without the # symbol.
E.g. MOV A, #n
Register- When the source (and oftentimes the destination) is a register in the instruction. The registers A, DPTR, R0-R7can be used in register addressing mode.
E.g. MOV A, Rn (where n = 0,…..7)

## Slide 6: Addressing modes
Direct – The Direct addressing mode allows all 128 bytes of the RAM/SFR to be addressed using the single byte address allocated to the memory location. RAM locations are addressed using addresses 00h-7Fh whilst SFRs use 80h-FFh
E.g. MOV A, madd (madd is a byte value)
Indirect- a register or memory address can hold the value of the eventual source or destination address. The data to be used can be said to be indirectly accessible this way. The mnemonic symbol used to indicate an indirect addressing mode is the @ symbol/sign.
E.g. MOV @Rp, #n (p is a value between 0 and 7)

## Slide 7: Illustration of Addressing Modes for Data Movement

## Slide 8: MOV Instruction
The Move instruction covers movement of data without modification of the operands.
Variations include MOVX (when moving to external data memory location) and MOVC (when moving to program memory location)

## Slide 9: MOVX and MOVC Instructions

## Slide 10: PUSH and POP instructions
The push instruction copies data from the source address to the stack(SP- SP is a special function register is incremented by one) e.g. PUSH add.
The pop instruction copies data from the stack (SP is decremented by one) to the destination address. E.g. POP add.

## Slide 11: PUSH and POP instructions

## Slide 12: XCH Instruction
This Instruction works in a bidirectional way. It moves instruction from source to destination and from destination to source.
Only Register, Direct and Indirect addressing modes can be used with it.
XCH instructions may also be used with a port location.
E.g. XCH A, Rn (n = 0, 1……..7)

## Slide 13: Summary